JIANGSU SOHO VIETNAM   CO . , LTD

STREET LED LIGHTING BETTER LIGHTING

Add:No.3, Cau Buou Commercial Centre, Ta Thanh Oai, Thanh Tri, Hanoi

E: soholedlighting@gmail.com            T:0934 422389            www.denchieusangcongtrinh.com.vn

Quotation for LED street light Better Lighting

Báo giá đèn đường LED Better Lighting

| Model NO. | Specification | Unit price |
| --- | --- | --- |
| SH-BTLED-1601A-120W （we have patent for this new product） | Power: 120W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 144 pcs CCT.: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: PHILIPS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size:798*380*163MM Warranty: 5 years REMARK: we have two kind of spigot : small one is for 38-50MM pole, big one is for 60mm pole PCB area is 8mm thick, so we can drill any hole according to your different PCB design | USD 123/PC (With cut-off switch) USD 121/PC (Without cut-off switch) Empty fitting without PCB and lens: USD69 /pc |
| SH-BTLED-1601A-150W | Power: 150W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 192 pcs CCT.: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: PHILIPS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size:798*380*163MM Warranty: 5 years REMARK: we have two kind of spigot : small one is for 38-50MM pole, big one is for 60mm pole PCB area is 8mm thick, so we can drill any hole according to your different PCB design | USD 131/PC (With cut-off switch) USD 129/PC (Without cut-off switch) Empty fitting without PCB and lens: USD69 /pc |
| SH-BTLED-1601A-180W | Power: 180W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 240 pcs CCT.: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: PHILIPS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size:798*380*163MM Warranty: 5 years REMARK: we have two kind of spigot : small one is for 38-50MM pole, big one is for 60mm pole PCB area is 8mm thick, so we can drill any hole according to your different PCB design | USD 145/PC (With cut-off switch) USD 143/PC (Without cut-off switch) Empty fitting without PCB and lens: USD69 /pc |
| SH-BTLED-1601B-80W | Power: 80W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 108 pcs Color temperature: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: PHILIPS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size: 670*310*145 MM Warranty: 5 years | USD 94/PC (With cut-off switch) USD 91/PC (Without cut-off switch) Empty fitting without PCB and lens: USD49 /pc |
| SH-BTLED-1601B-100W | Power: 100W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 144 pcs Color temperature: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: PHILIPS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size: 670*310*145 MM Warranty: 5 years | USD 98/PC (With cut-off switch) USD 96/PC (Without cut-off switch) Empty fitting without PCB and lens: USD49 /pc |
| SH-BTLED-1601C1-60W/40W | Power: 60W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 72 pcs Color temperature: 3000-6500K CRI: >70 Average lumen: 110 lm/W Driver brand: INVENTRONICS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size:550(450)*240*110mm Warranty: 5 years Power: 40W LED chip brand: LUMILEDS 3030 chip LED chip quantity: 48pcs Color temperature: 3000-6500K CRI: >70 Total lumens: 4400 lm Average lumen: 110 lm/W Driver brand: INVENTRONICS SPD: 10KV+10KA IP rating: IP66 IK rating: IK08 Fitting size:550(450)*240*110mm Warranty: 5 years | USD 77/PC (With cut-off switch) USD 75/PC (Without cut-off switch) Empty fitting without PCB and lens: USD36 /pc USD 74/PC (With cut-off switch) USD 72/PC (Without cut-off switch) Empty fitting without PCB and lens: USD36 /pc |

# Text boxes

NEW

NEW

NEW

NEW

NEW

NEW